## Slide 1: D-JOLT: Distant Jolt Prefetcher
Tomoki Nakamura, Toru Koizumi, Yuya Degawa, Hidetsugu Irie, Shuichi Sakai, Ryota Shioya
{tomokin, koizumi, degawa, irie, sakai}@mtl.t.u-tokyo.ac.jp, shioya@ci.i.u-tokyo.ac.jp
Notes: Thank you for the introduction.
Hello.
My name is Tomoki Nakamura.
I’d like to begin the presentation with the title D-JOLT: Distant Jolt Prefetcher.

## Slide 2: Introduction
Instruction prefetchers can effectively reduce instruction cache misses
We propose a Distant Jolt (D-JOLT) prefetcher.
  New signature generation algorithm
    Using the number of successive returns improves performance.
  Hybrid of long-range, short-range and fallback prefetcher
    Long-range prefetcher has long distance.
    Long distance improves not only the timeliness but also the coverage.
D-JOLT achieves 28.9% IPC speedup over no prefetching, close to an ideal model.
Notes: In recent applications, L1I cache misses are performance bottlenecks.
Instruction prefetchers can effectively reduce instruction cache misses.
We propose a Distant Jolt (D-JOLT) prefetcher.
D-JOLT consists of two main ideas.
First, D-JOLT uses new signature generation algorithm.
The algorithm improves performance with using the number of successive returns.
Seconds, D-JOLT is a hybrid of three prefetchers with different characteristics.
Long-range prefetcher, one of hybrid, has long distance and improves not only the timeliness but also the coverage.
D-JOLT achieves 28.9% IPC speedup over no prefetching, close to an ideal model.

## Slide 3: Topics
Baseline prefetcher and its three parameters
Observation of the three parameters
Approach
Design
Evaluation
Conclusion
Notes: These are the topic of my presentation.

## Slide 4: Baseline: RAS-directed instruction prefetching (RDIP)
RDIP Algorithm
  Generates a signature by hashing all the PCs recorded in a return-address-stack (RAS)
  Learning:
    Records miss addresses in associated with the signature
  Prediction:
    Prefetches the miss addresses associated with the signature upon every signature change
Learning
Prediction
Cache Miss Addr.
RAS
RAS
Issuing Prefetch
hash()
hash()
sig.
sig.
Notes: First, the baseline prefetcher of our proposal prefetcher is explained.
It’s a RAS-directed instruction prefetching (RDIP).
The RDIP generates a signature by hashing all the PCs recorded in a return-address-stack (RAS).
In general, RAS is a mechanism for recording return addresses of function calls used for branch target prediction.
As shown the left figure, when cache miss occurs, the RDIP records the miss addresses in associated with the signature.
Then, as shown the right figure, the RDIP prefetches the cache miss addresses associated with the signature upon every signature change.

## Slide 5: Call Stack Chart for analysis
This figure shows call stack depth changes.
  It changes for each call/return instruction.
Horizonal axis :
  call stack depth
Vertical axis :
  execution of instructions
Each block :
  A dynamic instruction sequence with a call/return instruction at the end
  We call this block a code block.
A: call |  |  | 
 | B: call |  | 
 |  | C: call | 
 |  |  | D: ret
 |  | E: call | 
 |  |  | F: ret
 |  | G: ret | 
 | H: call |  | 
execution
call stack depth
Call is fetched
Return is fetched
Code
block
return
call
Notes: Next, to discuss, I introduce the following figure.
This figure is call stack chart , which represents call stack depth changes for each call/return instructions.
The horizonal axis shows call stack depth and the vertical axis shows execution of instructions.
Each block shows a dynamic instruction sequence with a call/return instruction at the end.
We call this block a code block.
When a call instruction is fetched, the next block shifts to the right.
And, when a return instruction is fetched, the next block shifts to the left.

## Slide 6: RDIP analysis using Call Stack Chart
We introduce the following three parameters to discuss.
  Siggen:
  Histlen
  Distance
A: call |  |  | 
 | B: call |  | 
 |  | C: call | 
 |  |  | D: ret
 |  | E: call | 
 |  |  | F: ret
 |  | G: ret | 
 | H: call |  | 
execution
call stack depth
Call is fetched
Return is fetched
Notes: Using this figure, I’ll introduce the following three parameters to discuss, siggen, histlen and distance.

## Slide 7: The 1st parameter: Siggen
Siggen: a type of signature generation algorithm
RASWHOLE: the siggen used in the RDIP
  Uses all the PCs recorded in the RAS.
execution
call stack depth
Current
A: call |  |  | 
 | B: call |  | 
 |  | C: call | 
 |  |  | D: ret
 |  | E: call | 
 |  |  | F: ret
 |  | G: ret | 
 | H: call |  | 
Signature = Hash(A,B,C)
RAS: [A]
RAS: [A,B]
RAS: [A,B,C]
RASWHOLE
Notes: The first parameter is a siggen.
We call a type of signature generation algorithm siggen.
The siggen used in the RDIP generate signature using all the PCs recorded in the RAS.
The siggen is called as RASWHOLE.
In the figure, after call c fetched, RAS contains A, B, and C.
And, siggen generate the signature using all entries, A, B, and, C.

## Slide 8: The 2nd parameter: Histlen
A: call |  |  | 
 | B: call |  | 
 |  | C: call | 
 |  |  | D: ret
 |  | E: call | 
 |  |  | F: ret
 |  | G: ret | 
 | H: call |  | 
A histlen is the number of PCs used to generate a signature.
Using a longer histlen…
  improves the prediction accuracy.
  decreases the capacity efficiency.
execution
call stack depth
Histlen = 3
Current
Signature = Hash(A,B,C)
RAS: [A,B,C]
Notes: The second parameter is a histlen.
A histlen is the number of PCs used to generate a signature.
In the figure, after call c fetched, RAS contains A, B, and C.
In this case, the histlen is 3.
Using a longer histlen increases the number of signatures.
This improves the prediction accuracy.
On the other hand, it decreases the capacity efficiency.

## Slide 9: The 3rd parameter: Distance
We introduce a distance, the number of code blocks
  from a code block where prefetch is issued
  to a code block of a prefetch target.
In this figure, the distance is five.
  Actually, in the RDIP, the distance is one.
A: call |  |  | 
 | B: call |  | 
 |  | C: call | 
 |  |  | D: ret
 |  | E: call | 
 |  |  | F: ret
 |  | G: ret | 
 | H: call |  | 
9
execution
prefetch
Distance = 5
Current
Signature = Hash(A,B,C)
RAS: [A,B,C]
Notes: The third parameter is a distance.
We introduce a distance is the number of code blocks from the code block when issuing prefetch to the code block of a prefetch target.
In this figure, the orange code block is a prefetch target when call c is fetched.
In this case, the distance is 5.
Actually, in the RDIP the distance is one.

## Slide 10: The 3rd parameter: Distance
When the distance is increased,
  prefetches can be issued earlier,
  but it can decrease the prediction accuracy.
A |  |  | 
 | B |  | 
 |  | C | 
A |  |  | 
 | B |  | 
 |  | C | 
Distance = 7
Distance = 2
Notes: When the distance is increased, prefetches can be issued earlier than demand accesses.
On the other hand, it can decrease the prediction accuracy because the prefetcher predicts the distant future.

## Slide 11: Topics
Baseline prefetcher and its three parameters
Observation of the three parameters
Approach
Design
Evaluation
Conclusion
Notes: Next, I’d like to explain our observation of the three parameters.

## Slide 12: The 1st observation: Weak Point of RASWHOLE siggen
The prediction accuracy decreases when return functions are successive.
  Reason1) The number of valid entries decreases.
    Entries are popped from RAS when return is fetched
  Reason2) Recent history of calls is lost.
A: call |  |  | 
 | B: call |  | 
 |  | C: call | 
 |  |  | D: ret
 |  | E: call | 
 |  |  | F: ret
 |  | G: ret | 
 | H: call |  | 
Current
Signature = Hash(A)
RAS: [A,B,E]
RAS: [A,B]
RAS: [A]
RAS: [A,B,C]
RAS: [A,B]
RAS: [A,B]
RAS: []
RAS: [A]
Notes: The first is a weak point of RASWHOLE siggen.
In RASWHOLE, the prediction accuracy decreases when return functions are successive.
The first reason is that the number of valid entries decreases.
That’s because entries are popped from RAS when return is fetched.
The second reason is that the latest history of calls is lost.
The figure shows that, after return F and return G fetched, the RAS contains only call A.

## Slide 13: The 2nd observation: Longer Histlen
A longer histlen does not increase explosively the number of signatures.
  Even a long histlen does not require the capacity so much.
This is because call flow variations is smaller than branch instructions path variation.
Chart: Histlen
| 1 | 2 | 3 | 4 | 5 | 6 | 7
Client | 0.45142 | 0.66356 | 0.84538 | 1 | 1.1823 | 1.3703 | 1.4836
Server | 0.69529 | 0.79543 | 0.89613 | 1 | 1.0572 | 1.1252 | 1.2135
SPEC | 0.32074 | 0.52018 | 0.74248 | 1 | 1.2681 | 1.5662 | 1.8972
The normalized number of signatures
Does not increase explosively
(Histlen 4 is used in RDIP)
Notes: The second is a longer Histlen.
We found that a longer histlen does not lead to an explosive increase in the number of signatures.
The figure shows the number of signature for each histlen.
The trace distributed by IPC1 website was used for this investigation.
The traces was divided into 3 groups of client, server and spec.
The value is normalized by those of Histlen4, which is used in RDIP.
The result shows that, even in histlen7, the number of signatures increase less than twice as much as those of histen4.
This is because call flow variations is smaller than branch instructions path variation.

## Slide 14: The 3rd observation: Strong Point of Long Distance
In the RDIP, the distance is fixed to one.
However, using a long distance improves the coverage.
We explain the case of distance 4 using call stack charts.
Notes: The third is a strong point of long Distance.
In the RDIP, the distance is fixed one.
However, we found that using a long distance improves the coverage.
Using call stack charts, I’ll explain the case of distance 4.

## Slide 15: The 3rd observation: Strong Point of Long Distance
X0 |  |  | 
 | X1 |  | 
 | P1 |  | 
 | P2 |  | 
Learning: Addresses in multiple code blocks (e.g., P1 and P2) are associated with one signature (H(X0,X1)) as prefetch targets.
(b) flag == false
Distance = 4
Distance = 4
X1();
if(flag){F();}
P1();
(a) flag == true
X0 |  |  | 
 | X1 |  | 
 | F |  | 
 | P1 |  | 
 | P2 |  | 
sig. = H(X0,X1)
Notes: Let’s consider the source code with a function F in if statement.
The left figure shows a call stack chart when flag is true.
And, the right figure shows a call stack chart when flag is false.
In the left side, a code block P1 is associated with signature H(X0, X1).
In the right side, a code block P2 is associated with same signature H(X0, X1).

## Slide 16: The 3rd observation: Strong Point of Long Distance
X0 |  |  | 
 | X1 |  | 
 | P1 |  | 
 | P2 |  | 
On each signature, addresses in multiple code blocks are predicted.
Addresses in the same code blocks are prefetched in association with multiple signatures.
prefetch
One signature prefetches multiple code blocks
X0 |  |  | 
 | X1 |  | 
 | P1 |  | 
 | P2 |  | 
prefetch
prefetch
b. One code block is prefetched
by multiple signatures
Notes: Results of the learning, as shown the left figure, on each signature, addresses in multiple code blocks are predicted.
As shown the right figure, addresses in the same code blocks are prefetched in association with multiple signatures.
The longer the distance, the more the number of if statements included code blocks and the learning.

## Slide 17: The 3rd observation: Strong Point of Long Distance
The learning
  Improves the coverage and reduces cache misses.
  Decreases the prediction accuracy slightly.
Chart: Distance
| 0 | 1 | 2 | 3 | 5 | 7 | 9
Uncovered rate | 0.49282 | 0.28026 | 0.17537 | 0.11907 | 0.083966 | 0.076458 | 0.074688
Accuracy | 0.88218 | 0.88083 | 0.87537 | 0.86316 | 0.83635 | 0.81264 | 0.79447
accuracy
The normalized # of misses
The accuracy slightly decreases.
The number of misses significantly decreases.
(Distance 1 is used in RDIP)
Notes: The learning improves the coverage with few reduction in the accuracy.
This graph shows the normalized number of misses and accuracy with different distances.
The results shows a longer distance reduces the number of cache misses significantly.
While the prediction accuracy slightly decreases.

## Slide 18: Topics
Baseline prefetcher and its three parameters
Observation of the three parameters
Approach
Design
Evaluation
Conclusion
Notes: Next, I’d like to explain our approach.

## Slide 19: Approach
Based on the observations, we propose the D-JOLT prefetcher.
D-JOLT uses a new Siggen, FIFORETCNT, instead of RASWHOLE.
D-JOLT takes hybrid configuration.
  Long-range: distance 15, histlen 7
  Short-range: distance 4, histlen 4
  Fallback: Stream, degree 2
Notes: Based on the observation, we propose the D-JOLT prefetcher.
D-JOLT consists of two main ideas.
First, D-JOLT uses a new Siggen, FIFORETCNT, instead of RASWHOLE.
Seconds, D-JOLT takes hybrid configuration of different characteristics, long-range, short-range and fallback prefetcher.

## Slide 20: 1. FIFORETCNT
Generates a signature by hashing following values
  Call PCs: recent call PCs recorded in FIFO
  Return Count: the number of successive returns
・・・
A: call |  |  | 
 | B: call |  | 
 |  | C: call | 
 |  |  | D: ret
 |  | E: call | 
 |  |  | F: ret
 |  | G: ret | 
 | H: call |  | 
call stack depth
Current
Signature = Hash(B,C,E,2)
FIFO: [B,C,E], ret count: 0
FIFO: [B,C,E], ret count: 1
FIFO: [B,C,E], ret count: 2
FIFO: [], ret count: 0
FIFO: [A], ret count: 0
FIFO: [A,B], ret count: 0
FIFO: [A,B,C], ret count: 0
FIFO: [A,B,C], ret count: 1
FIFO size=3
Notes: First of all, FIFORETCNT generates a signature by hashing following values.
The first is a call PC.
It uses recent call PCs recoded in a FIFO.
The second is return count, the number of successive returns.
In this figure, after return G fetched, FIFORETCNT generate signature using B, C and E and return count, 2.

## Slide 21: 1. Strong Point of FIFORETCNT
Strong Points
  Uses latest history of call functions
  Keeps the histlen long
    Changes the signature without discarding the FIFO information
A |  |  | 
 | B |  | 
 |  | C | 
 |  |  | D
 |  | E | 
 |  |  | F
 |  | G | 
 | H |  | 
A |  |  | 
 | B |  | 
 |  | C | 
 |  |  | D
 |  | E | 
 |  |  | F
 |  | G | 
 | H |  | 
Signature = FIFORETCNT(B,C,E,0)
Signature = RASWHOLE(A,B,E)
RASWHOLE
FIFORETCNT
Notes: Using this figure, I’ll explain a strong point of FIFORETCNT against RASWHOLE.
After call E fetched, RASWHOLE contains A, B and E.
And, FIFORETCNT contains B, C and E.

## Slide 22: 1. Strong Point of FIFORETCNT
Strong Points
  Uses latest history of call functions
  Keeps the histlen long
    Changes the signature without discarding the FIFO information
A |  |  | 
 | B |  | 
 |  | C | 
 |  |  | D
 |  | E | 
 |  |  | F
 |  | G | 
 | H |  | 
A |  |  | 
 | B |  | 
 |  | C | 
 |  |  | D
 |  | E | 
 |  |  | F
 |  | G | 
 | H |  | 
Signature = FIFORETCNT(B,C,E,1)
Signature = RASWHOLE(A,B)
RASWHOLE
FIFORETCNT
Notes: After returns F fetched, in RASWHOLE, call E is popped.
On the other hands, in FIFORETCNT, call E remains and the return counter is incremented.

## Slide 23: 1. Strong Point of FIFORETCNT
Strong Points
  Uses latest history of call functions
  Keeps the histlen long
    Changes the signature without discarding the FIFO information
A |  |  | 
 | B |  | 
 |  | C | 
 |  |  | D
 |  | E | 
 |  |  | F
 |  | G | 
 | H |  | 
A |  |  | 
 | B |  | 
 |  | C | 
 |  |  | D
 |  | E | 
 |  |  | F
 |  | G | 
 | H |  | 
Signature = FIFORETCNT(B,C,E,2)
Signature = RASWHOLE(A)
RASWHOLE
FIFORETCNT
Notes: After successive return G fetched, RASWHOLE contains only call A.
On the other hands, FIFORETCNT contains call B, C, and E.
And, the return counter is incremented to 2.
In this way, FIFORETCNT can use latest history of call functions and changes the signature without discarding the entries.

## Slide 24: 2. Hybrid configuration
D-JOLT takes a hybrid configuration.
  Long-range prefetcher
  Short-range prefetcher
  Fallback prefetcher
Using a figure, we explain their issuing prefetches.
Notes: Second, D-JOLT takes a hybrid configuration of the following three prefetchers, Long-range, short range and fallback prefetcher.
Using a figure, I explain their issuing prefetch.

## Slide 25: 2. Hybrid configuration
Long history
Long distant
Current
Long-range
Predicts addresses in a distant code block(s)
Uses long distance and history
Notes: Long-range prefetcher intend to predict addresses in a distant code block using long history.
To realize it, long-range has long distance and long histlen.

## Slide 26: 2. Hybrid configuration
Recent history
Short distant
Current
In preparation for failure of long-range prefetcher,
  predicts addresses for the near future
High accuracy due to predict the near future
Short-range
Predicts addresses in a distant code block(s)
Uses long distance and history
Long-range
Notes: In preparation for failure of long-range prefetcher, the short-range prefetcher predict the address in the code block(s).
Due to predict the near future, short-range has high accuracy.
To realize it, short-range has a short distance and histlen.

## Slide 27: 2. Hybrid configuration
Stream Prefetch
Long-range
Short-range
Fall back
Current
Issues stream prefetch afterwards if short-range fails
Predicts addresses in a distant code block(s)
Uses long distance and history
In preparation for failure of long-range prefetcher,
  predicts addresses for the near future
High accuracy due to predict the near future
Notes: Fallback prefetcher is a modest stream prefetcher.
When the former two prefetchers fail in address prediction and cache misses occur, the fallback issues stream prefetch afterwards.

## Slide 28: Topics
Baseline prefetcher and its three parameters
Observation of the three parameters
Approach
Design
Evaluation
Conclusion
Notes: Next, I’d like to explain the design of our proposal method.

## Slide 29: Generate signature
Sig queue
Miss Table
distance = n
Siggen
Call / Return
Generated new signature
Pop the oldest signature
Notes: D-JOLT mainly consists of siggen, sig queue and miss table.
A sig queue is a mechanism to realize the distance.
A sig queue records recent signatures for the number of distance.
A miss table records miss addresses association with signature.
First, I explain about generation of signatures.
When a call or return is fetched, siggen generate a new signature.
The signature is pushed to the sig queue, and the oldest signature is popped.

## Slide 30: Learning missed address
Siggen
Sig queue
missed addr.
Miss Table
n-th previous
signature
distance = n
Notes: Next, the flow of learning.
When L1I cache miss occurs, D-JOLT gets the signature, which is the tail of the sig queue.
Because the number of entries n in the Sig queue represents the distance, the tail is n-th previous signature.
The miss line address is recorded in the miss table in association with this signature.

## Slide 31: Prediction
Siggen
Sig queue
Call / Return
Issuing prefetch addr.s
Generated new signature
Miss Table
Notes: Finally, the flow of prediction.
When a call or return is fetched, siggen generate a new signature.
On prediction, D-JOLT use the signature without going through the sig queue.
D-JOLT get addresses associated with the signature from miss table and issues prefetching the addresses.
Because the signature that does not go through the Sig queue is used, D-JOLT predicts the distant future.

## Slide 32: Topics
Baseline prefetcher and its three parameters
Observation of the three parameters
Approach
Design
Evaluation
Conclusion
Notes: Next, I’d like to show the performance of D-JOLT.

## Slide 33: Evaluation Environment
IPC1 single core configuration
Evaluate the following prefetchers and an ideal model
  Next 3lines Prefetcher
  Boomerang
  Shotgun
  RDIP
  ideal
  D-JOLT
Notes: We simulated D-JOLT using IPC1 single core configuration.
D-JOLT prefetcher was compared against the following prefetchers and an ideal model.

## Slide 34: IPC speedup over no prefetching
Chart: 
| Geomean of 8 Client Traces | Geomean of 35 Server traces | Geomean of 7 SPEC traces | Geomean of all 50 traces
Next 3lines | 1.0536 | 1.1552 | 1.0214 | 1.1189
Boomerang | 1.0423 | 1.2061 | 1.0169 | 1.1504
Shotgun | 1.0452 | 1.1736 | 1.0263 | 1.1306
RDIP | 1.0614 | 1.3159 | 1.0336 | 1.2292
D-JOLT | 1.0847 | 1.397 | 1.0493 | 1.2889
ideal | 1.1111 | 1.3983 | 1.065 | 1.2974
Notes: First, this figure shows IPC.
The horizontal axis represents the workloads, and the vertical axis represents the IPC speedup over no prefetching.
The orange blocks show D-JOLT.
D-JOLT shows higher performance than existing prefetchers in over all workloads.
In server workloads,
D-JOLT achieved performance improvement close to the ideal model.
In geomean, the performance improves by 28.9% against no prefetching.

## Slide 35: L1I MPKI
Chart: 
| Geomean of 8 Client Traces | Geomean of 35 Server traces | Geomean of 7 SPEC traces | Geomean of all 50 traces
No prefetch | 10.4679 | 41.9262 | 7.3328 | 26.306
Next 3lines | 7.7112 | 29.8814 | 6.1238 | 19.2709
Boomerang | 8.6782 | 25.4202 | 6.7795 | 17.7886
Shotgun | 8.1172 | 28.5204 | 6.0469 | 18.7728
RDIP | 4.7861 | 16.8618 | 3.7363 | 11.1628
D-JOLT | 1.0082 | 0.85959 | 0.84171 | 0.87922
Notes: Next, the figure shows L1I Miss per Kilo instructions (MPKI).
The orange blocks show D-JOLT.
The D-JOLT significantly reduced the L1I MPKI to 3.0 or less for the all traces.

## Slide 36: Topics
Baseline prefetcher and its three parameters
Observation of the three parameters
Approach
Design
Evaluation
Conclusion
Notes: Finally, I’d like to explain conclusion.

## Slide 37: Conclusion
We propose a Distant Jolt (D-JOLT) prefetcher.
  New signature generation algorithm, FIFORETCNT
  Hybrid of long-range, short-range and fallback prefetcher
D-JOLT prefetcher achieves 28.9% speedup in geomean over no instruction prefetching.
Notes: We propose D-JOLT prefetcher, which consists of two main ideas.
First, D-JOLT uses new siggen, FIFORETCNT.
Seconds, D-JOLT takes a hybrid configuration of long-range, short-range and fallback prefetcher.
D-JOLT prefetcher achieves 28.9% speedup in geomean over no prefetching.
Thank you for your listening.