## Slide 1: The FNL-MMA instruction cache prefetcher
André Seznec
INRIA/IRISA

## Slide 2: The I-cache issue
High miss rates on new servers and client applications
No easy access to traces of applications with large instruction footprint.
  ☞ Thanks to the IPC organizers

## Slide 3: Prefetching issues
When to trigger prefetches ?
  On misses: too late
  On every access: too many
          ➡︎ Somewhere between ..
Which lines to prefetch ?
  Next line(s)
  Consecutively used lines
          ➡︎ Need both
How to prefetch timely ?

## Slide 4: The I-Shadow cache
A small tag cache for demand misses
  3-way 64-entry:
    < I-cache size, but not that much
  Miss on I-cache without prefetching
    ➡︎ also I-Shadow miss
      ➡︎Trigger prefetch on I-Shadow miss

## Slide 5: Next-line prefetching is working some kind of
Next line on I-Shadow misses
  1.093 speed-up
  45 % extra L2 accesses 🥶
5 next lines on I-Shadow misses:
  1.087 speed-up
  3x extra L2 accesses ☠️
Let us get rid of these extra L2 accesses

## Slide 6: Footprint Next Line prefetcher
Prefetch next-line(s) only if (very likely) to be used
  And several cache lines !!
      ➡︎Predict the next line(s) footprint

## Slide 7: Predicting next-line use (1)
Two (large) direct-mapped tables to monitor application footprint
Touched : 1 bit
WorthPF: 2 bits

## Slide 8: Predicting next-line use (2)
On an I-Shadow cache miss on block B
Set Touched[B]
1
If Touched[B-1]
WorthPF[B-1]=3
1
3
If WorthPF[B] prefetch B+1
and B+2 and B+3, but not B+4
0
1
1
2

## Slide 9: « Used in a reasonable future »
Smart resetting for Touched and WorthPF
  every 8K I-Shadow misses
    If Touched[B] WorthPF[B]--; Touched[B]=0;

## Slide 10: FNL evaluation
64Kentry i.e. 24 KB
Up to 1 line: 1.124
Up to 3 lines: 1.159
Up to 5 lines: 1.165
➜ 1.148 with 3KB
Much better than pure next-line prefetching
at a limited 11.8 % extra L2 accesses

## Slide 11: Prefetching consecutively used blocks
Without prefetcher,
miss on B is « often followed » by miss on C
Intuition:
  Prefetch C !!
    Too late if one waits for the miss on B
    Prefetching destroys the correlation

## Slide 12: Next Miss Prefetcher
Use the I-Shadow cache
        ➡︎to predict the next I-cache miss
Associate B and C when
  B and C miss consecutively on I-Shadow AND C misses on the I-cache
Prefetch C after two successive occurences

## Slide 13: Next Miss prefetcher
Bb
Cc
I-shadow miss sequence
I-cache
miss
Associate C to Bb in the
Next Miss table
1.
I-cache
miss
Set (Bb,C) entry
to high confidence
2.
Prefetch C on
Bb I-Shadow miss
3 and more.

## Slide 14: Next Miss Prefetcher (3)
😎 Very accurate: 1% extra L2 accesses
🥶 Unfortunately often late:
  Halves the average miss latency
➽ Reasonable speed-up: 1.122
FNL + NMP: 1.226 speed-up
+23.1 % L2 accesses

## Slide 15: A step further: Multiple Miss Ahead prefetcher
B
B1
B2
B3
B4
B5
B6
B7
B8
B9
To avoid late prefetching: just prefetch earlier !!
I-shadow miss sequence
NMP
9-miss ahead

## Slide 16: MMA prefetcher
Triggered by I-Shadow cache miss
Associate B9 with B if
  B9 is 9th miss on I-Shadow after B AND B9 misses the I-cache
Prefetch after two successive occurrences

## Slide 17: The submitted prefetcher
FNL5+MMA9: Up to 5 next-line + 9-miss ahead
  FNL5: 64Kentries Touched and WorthPF
    24 KB
  MMA9: 8Kentries 9-miss ahead table
    71 bits per entry: 58 (addr) +12 (tag) +1
    71 KB
1.287 speed-up
38.3 % extra L2 accesses
91.8 % miss reduction

## Slide 18: Extra filters (not useful on Championship framework, but needed on effective hardware)
Filter FNL5 requests:
  block B-1 recently prefetched or missing I-Shadow ➡︎ only try to prefetch B+5
Filter MMA requests:
  Do not prefetch again recently prefetched blocks

## Slide 19: Further experiments (1)
The I-Shadow should be updated at commit time
(to avoid wrong path pollution)
Longer ahead distance ??
  FNL5+MMA30
    Speed-up : 1.284
    Extra L2 accesses: 48.5 %
  ➡︎ Tolerate prefetching at commit time

## Slide 20: Further experiments (2)
 | FNL5+MMA9 | FNL5 | MMA9
Full size (96KB) | 1.287 | 1.165 | 1.211
1/2th (48KB) | 1.284 | 1.163 | 1.186
1/4th. (24KB) | 1.273 | 1.158 | 1.133
1/8th (12KB) | 1.241 | 1.148 | 1.078
Combining FNL and MMA allows good performance
at reasonable storage budgets

## Slide 21: Prefetchers work in physical address space
MMA too !!:
  Smaller tables: 58 bits ➞ 42 bits address
FNL cannot cross page boundaries
1.284 speed-up

## Slide 22: Summary
FNL: prefetch only “useful” next lines
Multiple miss ahead:
  simple, accurate, and timely
  But needs huge miss ahead tables
FNL+MMA:
  Efficient combination with affordable storage budget

## Slide 23: An optimization developed after deadline
Better miss address prediction:
  1.293 speed-up
  95.9 % miss reduction

## Slide 24
Questions:
Andre.Seznec@inria.fr